## Slide 1
Most sophisticated sculpture
in the world
PRESENTER: 張語喬 OF HGSH
——the making of semiconductor

## Slide 2
Table of Contents
WHAT IS “MOSFET”
Introducing “MOSFET”
“PMOS” vs. “NMOS”
HOW ARE SEMICONDUCTORS MADE
Getting know about the manufacturing process of semiconductors

## Slide 3
03
SOURCE
SINK
GATE
Metal
Oxide
Semiconductor
MOSFET
Metal-Oxide-Semiconductor Field-Effect Transistor
  Commonly used in both analogue electronics and digital electronics
  The metal in “MOS” is usually replace by Poly-Silicon nowadays
The type of MOS depends on the elements doped in “source” and “sink”
  doping with P-type elements
PMOS
  doping with N-type elements
NMOS

## Slide 4
04
SOURCE
SINK
GATE
SOURCE
SINK
GATE
  Contains an extra Electron
  Missing one Electron
PMOS
NMOS
vs.
create “Electron hole”
Apply Voltage
Apply Voltage
Current

## Slide 5
Manufacturing
Process
05
OF SEMICONDUCTORS
Oxidation
Metallization
Photolithography
Etching
Adding “Gate”
Ion Implantation
Pad&Protective layer

## Slide 6
06
Oxidation
Thermal Oxidation Method
  The thickness of oxidation layer is determined by the duration of heating
  Using heat to create an layer of “Silicon dioxide” on the top of the wafer
  Normally, the temperature of the heating is between 900-1000℃
  Silicon dioxide layer and protect and insulate the wafer’s surface
Image source: Samsung

## Slide 7
07
  Common materials:
    Aluminum/Aluminum Alloy
    Copper
SOURCE
SINK
GATE
Metal
Oxide
Semiconductor
Metallization
  Using heat to grow an conductive layer on the top of Silicon dioxode
  Requires materials that are:
    having low resistance
    well adhered with the insulating layer
    won’t penetrate the insulting layer

## Slide 8
08
SILICON
SILICON DIOXIDE
METAL
1.Paint the wafer’s surface with “photoresist”
Photolithography
This process is aimed to create an protective layer on the designated area of the wafer’s surface
Photoresist is made with light-sensitive materials, and it’s design to change it chemical properties after being exposed to light.
You can create the pattern you want by controlling which part shall be exposed to light with “photomask”

## Slide 9
09
Pattern:
Same as the photomask
Pattern:
In contrast with the photomask
Positive
Negative
vs.
Two types of photoresist
Image source:
Wikipedia

## Slide 10
10
SILICON
SILICON DIOXIDE
METAL
1.Paint the wafer’s surface with “photoresist”
SILICON
SILICON DIOXIDE
METAL
2.Put on the “Photomask” and then irradiate the wafer
3.Using chemicals to corrode the photoresist that’s not attached to the wafer
SILICON
SILICON DIOXIDE
METAL
Photolithography
This process is aimed to create an protective layer on the designated area of the wafer’s surface

## Slide 11
11
Etching
Carving trenches on the surface that aren’t shielded by the photoresist layer
Remove the hard shell of photoresist
  Dry etching
using “plasma”
  Wet etching
using “liquid chemical”
SILICON
SILICON DIOXIDE
METAL
SILICON
SILICON DIOXIDE
METAL

## Slide 12
12
SILICON
SILICON DIOXIDE
METAL
Adding “Gate”
Putting on poly-silicon, metal, and dioxide layer as needed
Keeping the central part as “gate”, removing other areas through photolithographing and etching
SILICON
SILICON DIOXIDE
METAL

## Slide 13
13
SILICON
METAL
Ion Implantation
(Doping)
  Doping N-type or P-type elements(dopants) into semiconductors via “ion implantation” technique
Ion implantation is a low-temperature process, in which ions of one element are accelerated into a solid target

## Slide 14
13
Adding another dioxide layer for protection propercess
Carving out small holes(pad), then implant metal to complete the circuit.
SEMICONDICTOR
SEMICONDICTOR
SOURCE
SINK
GATE
Adding Pad&Protective Layer
Dioxide layer
It involves both “photolithography” and “etching” techniques to carve the pad

## Slide 15
Q&A
15

## Slide 16
Q&A
16
How to tell if an MOS is
PMOS or NMOS?

## Slide 17
Q&A
16
A:It depends on the dopants used in “Source” and “Sink”
How to tell if an MOS is
PMOS or NMOS?

## Slide 18
Q&A
17
How many steps in the making process that don’t involve “photolithography” and “etching”?

## Slide 19
Q&A
17
How many steps in the making process that don’t involve “photolithography” and “etching”?
A: Two(Oxidation&Metallization)

## Slide 20
Thanks for
Watching